## Slide 1
CS/EE/ME 75(C): Week 2 (3)
(with revised homework)
House Keeping:
  Course Zoom Link: https://caltech.zoom.us/j/282171019
  Hands-on review of last week’s Exercises: Free time on Thursday?
  Hands-on Zoom practice for Gazebo tutorial: Monday?
1) Our goal: Develop simulations for RC Car and Drive-o-copter
  Many control, planning, autonomy algorithms can be simulated
  Will simplify eventual integration.
2) First Steps
  Learn how to simulate using Gazebo, and visualize using RVIS
  Write a URDF/SDF

## Slide 2
Homework: Week 2 (3)
(revised homework)
Goal: become competent with Gazebo
  NOTE: Gazebo 9 is already installed in Ubuntu 18.1
  Read: “Beginner GUI” to get a sense of the Gazebo user interface layout
    http://gazebosim.org/tutorials?tut=guided_b2&cat=
  Next, visit the Gazebo “Build a Robot Tutorials” : http://gazebosim.org/tutorials?cat=build_robot . Complete the following tutorial steps under “Build a Robot”
    Read the “model structure and requirements” link: http://gazebosim.org/tutorials?tut=model_structure&cat=build_robot
      When you “clone” the githhub repository of Gazebo models (in the “The Model Database Repository” section), make sure the model directories get copied into /usr/share/gazebo-9/models/
    Read the “Make a Model” tutorial section http://gazebosim.org/tutorials?tut=build_model&cat=build_robot
      Create the “box.sdf” example. See the next page for in order to insert the model into gazebo through the GUI interface

## Slide 3
Homework: Week 2 (3)
(revised homework)
  Read the “Make a Model” tutorial section (continued)
    To insert the box into gazebo through the GUI interface, you must prepare the model for use in Gazebo:
      Make a directory : mkdir ~/.gazebo/models/box
      Put the box.sdf file in the box directory
      Put a model.config file in the box directory. Here is my example in the box on the right
    Start gazebo: gazebo &
    In the left panel, click on the “Insert” tab.
    You should see “The Box Model”under your models
    Click on the box model, and position it in your world
<?xml version="1.0"?>
<model>
<name>The Box Model</name>
<version>1.0</version>
<sdf version='1.5'>box.sdf</sdf>
<author>
<name>Joel Burdick</name>
<email>jburdick@caltech.edu</email>
</author>
<description>
The Box Tutorial Model
</description>
</model>

## Slide 4
Homework: Week 2 (3)
(revised homework)
    “Make a mobile Robot”: http://gazebosim.org/tutorials?tut=build_robot
      In this is a straightforward tutorial (it works with ROS melodic and the preinstalled gazebo-9.0.0 on Ubuntu 18.1) you will build a simple differential drive model
      I found no errors in this tutorial
      A lengthier version of this model-building exercise can also be found at:
        “Beginner: Model Editor:” ”: http://gazebosim.org/tutorials?tut=guided_b3 . This version creates basic solid components using the model editor, instead of the text-based creation in the “make a mobile robot”
    Carry out the “Attach Meshes” exercise (note, at the end of the “make a mobile robot” , there is a link to this exercise): http://gazebosim.org/tutorials?tut=attach_meshes&cat=build_robot
    Carry out the “add a sensor” tutorial: http://gazebosim.org/tutorials?tut=add_laser&cat=build_robot

## Slide 5
Homework: Week 2 (3)
(revised homework)
Visit the “Using a URDF in Gazebo” link on the tutorial page.
  http://gazebosim.org/tutorials/?tut=ros_urdf
  This tutorial is not so important, but it helps set up the following tutorials
  Before starting this tutorial, you must update gazebo/ros as follows
    Make sure that you are logged in as the super-user to your Ubuntu
    In a shell: sudo apt update
    In the same shell: sudo apt install ros-melodic-joint-state-publisher-gui
  Don’t forget to properly set your ROS and gazebo paths:
    In your catkin_ws space: source devel/setup.bash
    In your catkin_ws space: source /usr/share/gazebo-9/setup.sh
  The first important step in the tutorial is to carry out “Getting RRBot.” This model will be used in several steps
  Then carry out the steps of “View in Rviz” and “View in Gazebo”
  You can skim the rest of the tutorial

## Slide 6
Homework: Week 2 (3)
(revised homework)
Visit the “Using Roslaunch” link on the tutorial page.
  http://gazebosim.org/tutorials?tut=ros_roslaunch&cat=connect_ros
  Before attempting this tutorial, you must take two steps:
    Step #1: Change a line in the Gazebo 9 setup file: /usr/share/gazebo-9/setup.sh
      Original: export GAZEBO_MODEL_DATABASE_URI=http://gazebosim.org/models
      Corrected: export GAZEBO_MODEL_DATABASE_URI=http://models.gazebosim.org/
    Step #2: Load the Linux paths that you will need to make the tutorial work as listed:
      cd ~/catkin_ws
      source devel/setup.bash % source your compiled packages
      source /usr/share/gazebo-9/setup.sh % source paths needed by gazebo
      Source /opt/ros/melodic/setup.sh % sources paths needed by ROS
      Note: you can put these steps in your ~/.bashrc file so that these paths are loaded every time you start up a shell!