## Slide 1
CS/EE/ME 75(C): Week 3 (4)
(with revised homework)
House Keeping:
  Course Zoom Link: https://caltech.zoom.us/j/282171019
  Maybe another tutorial session on Friday?
1) Our goal: Develop simulations for RC Car and Drive-o-copter
  Many control, planning, autonomy algorithms can be simulated
  Will simplify eventual integration.
2) First Steps
  Learn how to simulate using Gazebo, and visualize using RViz
  Write an SDF for Gazebo, which will create an URDF for Rviz

## Slide 2
A simulator can mimic many (but not all) aspects of a real world robot deployment
  Simulate robot geometry & movements
  Simulate obstacles, objects in the robot’s environment
  Simulate sensor readings and sensor feedback process
  Simulate physical interactions between objects
    Most difficult & sensitive simulation
Why use simulation?
  Debug code before testing it in high-cost-of-failure real world situations
  Test on hardware which is not available
  Allow for parallel development across sub-teams
  Create visualization videos

## Slide 3
See tutorial at: http://gazebosim.org/tutorials?tut=guided_b2&cat=
Gazebo Simulation Architecture
Gazebo has two main parts/processes:
Server: Runs the physical simulation of the model world, and generates sensor signals/data
  gzserver
  Libraries: Transport, Sensors, Transport, Rendering
Client: Provides user interaction and visualization
  gzclient
  Libraries: Transport, Sensors, Transport, Rendering
Gazebo: run both gzserver & gzclient

## Slide 4
Elements of a Gazebo Simulation
Visual Object:
  Defines the geometry that is visualized in the GUI rendering
Collision Object:
  Defines geometry that is checked in physics simulation for collision
Sensor(s):
  Objects that collect, possiblyl process, and transmit data
Plugins:
  Bits of code that are embedded in simulations
World:
  Collection of models, lights, plug-ins and global parameters (that affect everything in the world)
Model:
  Collection of links (rigid bodies), joints, sensors, meshes (surface texture/color) and lights.
Link(s):
  Visual and Collision geometry of objects
Joints:
  Defines the constraints between links

## Slide 5
Models
A Model contains key properties
  Physical presence:
    Sphere, box, combination of shapes
    Kinematics: Joints & velocities
    Dynamics: mass, inertia friction, forces (e.g., gravity)
  Interface (optional)
    Control & feedback interface (libgazebo)
  A Model is described by two files
    Config file: model.config
    SDF file: <modelname>.sdf
Locations: /usr/share/gazebo-9/models/ (* standard gazebo models)
~/.gazebo/models/

## Slide 6
Models
<?xml version='1.0'?>
<sdf version="1.4">
<model name=“box.sdf">
<pose>0 0 0.5 0 0 0</pose> <!– origin -->
<static>true</static>
<link name="link">
<inertial>
<mass>1.0</mass>
<inertia> <!-- inertias -->
<ixx>0.083</ixx>
<ixy>0.0</ixy>
<ixz>0.0</ixz>
<iyy>0.083</iyy>
<iyz>0.0</iyz>
<izz>0.083</izz>
</inertia>
</inertial>
<collision name="collision">
<geometry>
<box>
<size>1 1 1</size>
</box>
</geometry>
</collision>
<visual name="visual">
<geometry>
<box>
<size>1 1 1</size>
</box>
</geometry>
</visual>
</link>
</model>
</sdf>
~/.gazebo/models/box/box.sdf
<?xml version="1.0"?>
<model>
<name>The Box Model</name>
<version>1.0</version>
<sdf version='1.5'>box.sdf</sdf>
<author>
<name>Joel Burdick</name>
<email>jburdick@caltech.edu</email>
</author>
<description>
The Box Tutorial Model
</description>
</model>
~/.gazebo/models/box/model.config

## Slide 7
Element Types in Models
Visual Geometry
  Physical appearance
    Simple Shapes: Sphere, box, shape combinations
    Complex Shapes: height maps, meshes
  Collision Geometry
    Shape used in physics simulation to check for interference, and model interaction forces
    Shape used for motion planning collision check
    Visual and shape geometries can be the same
    Usually, collision geometry is chosen as a simple bounding shape

## Slide 8
Element Types in Models
Joints
  Prismatic: 1 DOF “slider” joint allows translation
  Revolute: 1 DOF “hinge” joint allows rotation
  Revolute2: Two revolute joints in series
  Ball: 3 DOF “ball joint” (spherical joint)
  Universal: 2 DOF joint
  Screw: 1 DOF “helical” joint (threaded rod)
    Simple Shapes: Sphere, box, shape combinations
    Complex Shapes: height maps, meshes
  bounding shape

## Slide 9
Element Types in Models
Sensors
  Ray: produces range data, like a Lidar
  Camera:
    Simulate 2D camera
    Simulate 2D stereo cameras
    Simulate 3D RGB-D (like Kinect)
  Contact (“bump” sensor)
Lights
  Point Light: Omnidirectional source, like a light bulb
  Spot: Directional cone of light (spot light)
  Directional: parallel rays, like the sun

## Slide 10
Worlds
Composed of a model hierarchy
Gazebo server (gzserver) reads/parses a gazebo “world file” to generate and populate a world
  Formulated in Simulation Description Format (SDF) XML. Can also take URDF (which is then upgraded to SDF)
  File has a “.world” extension
  Contains all of the elements in a simulation
    Robots
    Static Objects
    Lights,
    Sensors
  Existing Gazebo Worlds: /usr/share/gazebo-9/worlds/

## Slide 11
General Gazebo/ROS Simulation Workflow
Steps
  Load a world:
    Gazebo <yourworld>.world &
      No ROS interface
    Roslaunch gazebo_ros <your_world>.launch &
      gazebo_ros can be replaced by other package names
      If you command the simulation from ROS
      If you want to use Rviz to view sensor output
  Robot(s) get “spawned” into the world
    There are multiple ways to do this
  Joint, robot states, sensor data are published
  Run Rviz, and subscribe to simulation data topics

## Slide 12
Homework: Week (3) 4
(revised homework from week 2 (3) )
Goal: become competent with Gazebo
  NOTE: Gazebo 9 is already installed in Ubuntu 18.1
  Read: “Beginner GUI” to get a sense of the Gazebo user interface layout
    http://gazebosim.org/tutorials?tut=guided_b2&cat=
  Next, visit the Gazebo “Build a Robot Tutorials” : http://gazebosim.org/tutorials?cat=build_robot . Complete the following tutorial steps under “Build a Robot”
    Read the “model structure and requirements” link: http://gazebosim.org/tutorials?tut=model_structure&cat=build_robot
      When you “clone” the githhub repository of Gazebo models (in the “The Model Database Repository” section), make sure the model directories get copied into /usr/share/gazebo-9/models/ directory
    Read the “Make a Model” tutorial section http://gazebosim.org/tutorials?tut=build_model&cat=build_robot
      Create the “box.sdf” example. See the next page for instructions on how to insert the model into gazebo through the GUI interface

## Slide 13
Homework: Week 2 (3)
(revised homework)
  Read the “Make a Model” tutorial section (continued)
    To insert the box into gazebo through the GUI interface, you must prepare the model for use in Gazebo:
      Make a directory : mkdir ~/.gazebo/models/box
      Put the box.sdf file in the box directory
      Put a model.config file in the box directory. Here is my example in the box on the right
    Start gazebo: gazebo &
    In the left panel, click on the “Insert” tab.
    You should see “The Box Model”under your models
    Click on the box model, and position it in your world
<?xml version="1.0"?>
<model>
<name>The Box Model</name>
<version>1.0</version>
<sdf version='1.5'>box.sdf</sdf>
<author>
<name>Joel Burdick</name>
<email>jburdick@caltech.edu</email>
</author>
<description>
The Box Tutorial Model
</description>
</model>
~/.gazebo/models/box/model.config

## Slide 14
Homework: Week 2 (3)
(revised homework)
    “Make a mobile Robot”: http://gazebosim.org/tutorials?tut=build_robot
      In this is a straightforward tutorial (it works with ROS melodic and the preinstalled gazebo-9.0.0 on Ubuntu 18.1) you will build a simple differential drive model
      I found no errors in this tutorial
      A lengthier version of this model-building exercise can also be found at:
        “Beginner: Model Editor:” ”: http://gazebosim.org/tutorials?tut=guided_b3 . This version creates basic solid components using the model editor, instead of the text-based creation in the “make a mobile robot”
    Carry out the “Attach Meshes” exercise (note, at the end of the “make a mobile robot” , there is a link to this exercise): http://gazebosim.org/tutorials?tut=attach_meshes&cat=build_robot
    Carry out the “add a sensor” tutorial: http://gazebosim.org/tutorials?tut=add_laser&cat=build_robot

## Slide 15
Homework: Week 2 (3)
(revised homework)
Visit the “Using a URDF in Gazebo” link on the tutorial page.
  http://gazebosim.org/tutorials/?tut=ros_urdf
  This tutorial is not so important, but it helps set up the following tutorials
  Before starting this tutorial, you must update gazebo/ros as follows
    Make sure that you are logged in as the super-user to your Ubuntu
    In a shell: sudo apt update
    In the same shell: sudo apt install ros-melodic-joint-state-publisher-gui
  Don’t forget to properly set your ROS and gazebo paths:
    In your catkin_ws space: source devel/setup.bash
    In your catkin_ws space: source /usr/share/gazebo-9/setup.sh
  The first important step in the tutorial is to carry out “Getting RRBot.” This model will be used in several steps
  Then carry out the steps of “View in Rviz” and “View in Gazebo”
  You can skim the rest of the tutorial

## Slide 16
Homework: Week 2 (3)
(revised homework)
Visit the “Using Roslaunch” link on the tutorial page.
  http://gazebosim.org/tutorials?tut=ros_roslaunch&cat=connect_ros
  Before attempting this tutorial, you must take two steps:
    Step #1: Change a line in the Gazebo 9 setup file: /usr/share/gazebo-9/setup.sh
      Original: export GAZEBO_MODEL_DATABASE_URI=http://gazebosim.org/models
      Corrected: export GAZEBO_MODEL_DATABASE_URI=http://models.gazebosim.org/
    Step #2: Load the Linux paths that you will need to make the tutorial work as listed:
      cd ~/catkin_ws
      source devel/setup.bash % source your compiled packages
      source /usr/share/gazebo-9/setup.sh % source paths needed by gazebo
      Source /opt/ros/melodic/setup.sh % sources paths needed by ROS
      Note: you can put these steps in your ~/.bashrc file so that these paths are loaded every time you start up a shell!